## Slide 1: An Eco-friendly Hybrid Urban Computing Network Combining Community-based Wireless LAN Access and Wireless Sensor Networking
Maarten Wijnants - Wim Lamotte
Hasselt University – EDM – iMinds | firstname.lastname@uhasselt.be
Nicolas Letor – Chris Blondia
University of Antwerp – iMinds – PATS | firstname.lastname@ua.ac.be
Eli De Poorter - Dries Naudts - Stijn Verstichel - Bart Lannoo - Ingrid Moerman
Department of Information Technology – iMinds – Ghent University | firstname.lastname@intec.ugent.be
Nelson Matthys - Christophe Huygens
iMinds–DistriNet - Department of Computer Science – KU Leuven | firstname.lastname@cs.kuleuven.be

## Slide 2
Integration of technology and computational power in public environments
Involves aspects from
  Pervasive computing
  Embedded computing
  Internet of Things (IoT)
Urban Computing
Hybrid
Network Combining
An Eco-friendly
Community-based WLAN Access
and Wireless Sensor Networking
Hybrid network consisting of 2 tiers
  Separate yet interfaced with each other
Wi-Fi crowdsourcing
  City residents are encouraged to share their wireless Internet connection
Guarantees city-scale access to digital information and Internet-based services
  Helps satisfy people’s continuously burgeoning desires and requirements with regard to ubiquitous information access and digital service consumption
Number of sensors deployed in the city
Enables dynamic aggregation of relevant environmental measurements and real-time status tracking of physical objects
  Scaffolds development of value-added end-user applications that are consumable through the community-powered access network
Societal attention for environmentalism and ecological sustainability is nearly becoming common practice
  Minimize ecological impact of products and services
Network includes measures to reduce environmental footprint of WSN subsystem
  Energy conservation

## Slide 3: Outline
Architectural Design
Composing Technologies and Features
  WSN Architecture
  Sensor Design and Hardware
  Community-based Wi-Fi Access
  Green Intelligence for Eco-friendly WSNs
  Application Framework
Proof-of-Concept Deployment
Example Urban Services
Conclusions

## Slide 4: Architectural Design
Integrated urban computing environment
  Multiple WSNs
  Community Wi-Fi network
  Back-end server LAN
  Intelligent “green” middleware

## Slide 5: Architectural Design
Wireless Sensor Network
  Capture information about physical space
  Transmit measurements to back-office

## Slide 6: Architectural Design
City-wide community-sustained Wi-Fi network
  Acts as uplink for WSNs
  Provides Internet access for end-users
  Cluster of wireless Access Points owned by volunteer citizens or governmental agencies

## Slide 7: Architectural Design
Back-end server LAN
  Persistent storage of WSN observations
  Centralized access to WSN data for authorized external parties
    Via relational DB
  Community manager and controllers for WLAN mobility solution

## Slide 8: Architectural Design
“Green” intelligence
  Distributed sensor reasoning framework
  Green WSN middleware
Distributed approach
  Limited intelligence on WSN nodes
    Local optimum
  Back-office coordinator
    Global optimum across all WSNs

## Slide 9: Outline
Architectural Design
Composing Technologies and Features
  WSN Architecture
  Sensor Design and Hardware
  Community-based Wi-Fi Access
  Green Intelligence for Eco-friendly WSNs
  Application Framework
Proof-of-Concept Deployment
Example Urban Services
Conclusions

## Slide 10: WSN Architecture
Involves heterogeneous types of devices
  Sensor nodes sense physical environment
    Lack routing functionality to reduce complexity
  Sensor routers provide multi-hop capabilities
    IPv6 Routing Protocol for Low-Power and Lossy Networks (RPL)
  Sensor gateway serves as sensor node uplink
    Internet access via community-based Wi-Fi network
Communication-wise exclusive use of standardized IEEE and IETF network protocols
  E.g., IEEE 802.15.4 and 6LoWPAN
  Sensor data transported to back-end via IETF CoAP (specialized RESTful web transfer protocol)

## Slide 11: Sensor Design and Hardware
Radio operates in 169 MHz frequency band
  Recently reallocated by European Commission
  Far less hindrance of obstacles & weather effects
    Lower dynamic link failures and boosted tx range
Backward compatibility with legacy sensor nodes via secondary 868 MHz RF transceiver

## Slide 12: Community-based Wi-Fi Access
Individual city-wide Wi-Fi community APs (CAPs)
  Wi-Fi sharing cfr Fon
  Geographically clustered into Virtual Access Areas
    All VAAs share one SSID
Virtual Private Ad Hoc Network (VPAN) overlay
  Securely connects CAPs with back-end servers
  Management and coordination in back-office

## Slide 13: Community-based Wi-Fi Access
End-user connects to CAP with Wi-Fi terminal
  No specialized software
Mobility solutions allow free roaming while consuming information
  Seamless intra-VAA session handover among constituting CAPs
  Transparent inter-VAA handover
    Slight service interruption

## Slide 14: Green Intelligence for Eco-friendly WSNs
Distributed sensor reasoning framework
  Configures sensor nodes for ecological operation
    Primarily in terms of energy expenditure
  Implemented at two separate levels
    Limited reasoning on individual sensor nodes to determine local energy consumption optimum through direct manipulation of proprietary low-level attributes
    Holistic reasoning on back-end coordinator to enforce a global optimum for each WSN as a whole
  Example configurable parameters include polling frequency, sleeping strategies, tx power, etcetera
  Sensor model designed as extension of the W3C Semantic Sensor Network Ontology

## Slide 15: Green Intelligence for Eco-friendly WSNs
Component and Policy Infrastructure (CaPI)
  Combination of component-based runtime and policy-driven management framework
    Components are coarse-grained, service-like functional units
    Policies are fine-grained scripts that encapsulate specific rules to govern runtime behavior of the sensor
  Allows for cost-effective reconfiguration and reorientation of WSN software over time
  Dynamic deployment of CaPI components and policies is controlled by the back-end
  Results in significant flexibility, removes need for expensive replacements of sensor software image and yields meaningful energy and operational savings

## Slide 16: Application Framework
Facilitates development of urban services
Separation of concerns design
  Clean division between sensor networks and services
  Relational database is enacted as go-between
    CoAP-based RESTful interface for sensor data storage
    HTTP-based RESTful interface for database querying
  Numerous advantages: simplified security, obsoletes IPv4/v6 protocol translation, declarative programming, …
Besides bare sensor measurements, DB maintains
  Hardware, software and network characteristics of WSNs
    Fed to green sensor intelligence via D2R engine
  Service-dependent information (scaffolds execution)

## Slide 17: Outline
Architectural Design
Composing Technologies and Features
  WSN Architecture
  Sensor Design and Hardware
  Community-based Wi-Fi Access
  Green Intelligence for Eco-friendly WSNs
  Application Framework
Proof-of-Concept Deployment
Example Urban Services
Conclusions

## Slide 18: Proof-of-Concept Deployment
Comprehensive Proof-of-Concept roll out in Ghent
  Belgian city with population of ~250.000 people
Involved sensor hardware : ~50 sensor nodes
Involved Wi-Fi hardware
  At least 10 CAPs, divided in 2 or 3 VAAs
    ~2 square kilometers Wi-Fi coverage
  Back-office: VAA Controllers (1 per VAA) and 1 VPAN Agent, Dimensioning Controller, Community Gateway
Objectives:
  Confirm technological validity of proposed architecture
  Evaluate qualitative features of dual design and services

## Slide 19: Proof-of-Concept Deployment
Emphasis on monitoring 2 distinct physical properties
  Depending on involved property, different sensors mounted on sensor board
  Car parking spaces
    Measure distortion of earth’s magnetic field in 3 spatial axes
    Deployed within “speeddisk”
  Garbage bin lid opening
    Magnet-activated reed switch

## Slide 20: Outline
Architectural Design
Composing Technologies and Features
  WSN Architecture
  Sensor Design and Hardware
  Community-based Wi-Fi Access
  Green Intelligence for Eco-friendly WSNs
  Application Framework
Proof-of-Concept Deployment
Example Urban Services
Conclusions

## Slide 21: Personal Parking Assistant (PPA)
Outdoor parking control service for hand-helds
  Dynamically visualizes vacancy information pertaining to parking locations near a certain destination
Promising tool to alleviate the burden of searching for an available parking spot
Direct revenue for end-users
  Witness an improvement of their urban life
Indirect benefit for the municipality stakeholder
  Positive impact on people’s perception of commuting
  Gains insight in parking patterns within their territory
    Could be exerted in future urban planning initiatives

## Slide 22: Garbage Bin Tampering Monitor (GBTM)
Public garbage bins for small-size litter disposal via a hole in their lid
  Cover needs to be removed to empty the dustbin
    Operation strictly reserved for municipal employees
Garbage bin sensor records lid opening/closing
Sensor observations and timestamps stored in DB
Web-based interface allows measurement retrieval
Objectives and advantages
  Facilitate detection of illegal activities (e.g., vandalism)
  Optimize garbage collection routes and timetables

## Slide 23: Outline
Architectural Design
Composing Technologies and Features
  WSN Architecture
  Sensor Design and Hardware
  Community-based Wi-Fi Access
  Green Intelligence for Eco-friendly WSNs
  Application Framework
Proof-of-Concept Deployment
Example Urban Services
Conclusions

## Slide 24: Conclusions
Proposed dual urban computing infrastructure integrates wireless sensing with community Wi-Fi
  The WSN architecture realizes physical sensing
  City-scale crowdsourcing of Wi-Fi access points guarantees pervasive Internet access
    Accommodates ubiquitous client-side digital service delivery
  Multi-faceted nature yields an end-to-end solution
    Operational chain spans from data registration at IoT node level all the way up to end-user service consumption via Wi-Fi
  Ecologically inspired measures (energy minimization)
Example urban services offer taste of myriad of enabled innovative and value-added services

## Slide 25: Thank You for Your Attention
Questions?